## Slide 1: Practical Universal Computers
Prof. Bienvenido Velez
Lecture 4
Bits
Wires
Gates
Turing Machines

## Slide 2: Outline
The von Neumann Architecture
  Big Ideas:
    Interpretation
    Stored program concept
Designing a simple processor
  Instruction Set Architecture
  Data Paths
  Control Unit

## Slide 3: The (John) Von Neumann Architecture (late 40’s)
I/O
devices
Central
Processing
Unit (CPU)
Memory
Allow communication
with outside world
Interprets instructions
Stores both programs and data
After 60 years … most processors still look like this!

## Slide 4: The von Neumann Architecture Central Processing (CPU)
I/O
devices
Central
Processing
Unit (CPU)
Memory
Control Unit
(FSM)
Data Paths
Interconnected registers,
muxes, decoders, …
control
status
active
passive

## Slide 5: Practical Universal Computers (John) Von Neumann Architecture (1945)
DataPaths
PC
ABR
ALU
AC
Program
Data
Memory
Control Unit
(FSM)
CPU
CPU + Memory makes up a universal TM
An interpreter of some programming language (PL)
status
control
This looks
just like a
TM Tape!!

## Slide 6: Von Neumann Architecture Key Ideas
Interpretation
Universal Computation
Stored Program Concept
In Simple Terms
A Practical Realization of a Universal Turing Machine

## Slide 7: Easy I Data Paths
A
D
D
R
E
S
S
B
U
S
Typically, designing a processor is an iterative
(aka trial end error) process
A0
A bus
A
B
AC
PC
ALU
D
A
T
A
B
U
S
DI

## Slide 8: The (John) Von Neumann Architecture The Memory Unit
I/O
devices
Central
Processing
Unit (CPU)
Memory
0 | 
1 | ADD A
2 | SUB B
3 | JUMP 1
 | A
 | B
 | …
N-1 | 
word size
address space

## Slide 9: The (John) Von Neuman Architecture Stored Program Concept
0 | 
1 | ADD A
2 | SUB B
3 | JUMP 1
 | A
 | B
 | …
N-1 | 
Program
Instructions
Program
Data
Programs and their data coexist in memory
Processor, under program control, keeps track of what needs to be interpreted as instructions and what as data.

## Slide 10: Definition Instruction Set Architecture
What it is:
  The programmers view of the processor
  Visible registers, instruction set, execution model, memory model, I/O model
What it is not:
  How the processors if build
  The processor’s internal structure

## Slide 11: Easy I A Simple Accumulator Processor Instruction Set Architecture (ISA)
Instruction Format (16 bits)
I
opcode
X
0
9
10
14
15
I = Indirect bit

## Slide 12: Easy I A Simple Accumulator Processor Instruction Set Architecture (ISA)
Name | Opcode | Action I=0 | Action I=1
Comp | 00 000 | AC ← not AC | AC <- not AC
ShR | 00 001 | AC ← AC / 2 | AC ← AC / 2
BrN(i) | 00 010 | AC < 0 ⇒ PC ← X | AC < 0 ⇒ PC ← MEM[X]
Jump(i) | 00 011 | PC ← X | PC ← MEM[X]
Store(i) | 00 100 | MEM[X] ← AC | MEM[MEM[X]] ← AC
Load(i) | 00 101 | AC ← MEM[X] | AC ← MEM[MEM[X]]
And(i) | 00 110 | AC ← AC and X | AC ← AC and MEM[X]
Add(i) | 00 111 | AC ← AC + X | AC ← AC + MEM[X]
Instruction Set
Easy all right … but universal it is!

## Slide 13: Easy I Memory Model
0 | 
2 | ADD A
4 | SUB B
6 | JUMP 1
 | A
 | B
 | …
512 | 
8 bits
8 bits

## Slide 14: Easy I A Simple 16-bit Accumulator Processor Instruction Set Architecture (ISA)
Accumulator (AC) is implicit operand to many instructions. No need to use instruction bits to specify one of the operands. More bits left for address and opcodes.
Although simple, Easy I is universal. (given enough memory). Can you see this?
Immediate bit specifies level of indirection for the location of the operand. I = 0: operand in X field (immediate). I=1 operand in memory location X (indirect).
Some Immediate Observations on the Easy I ISA

## Slide 15: Programming the Easy I
Compute the sum of the even numbers between 1 and N
int suma = 0;
Int count = 0;
For (count=2; count <= N; count += 2) {
suma += count;
}
High Level Language Version

## Slide 16: Programming the Easy I
Compute the sum of the even numbers between 1 and N
Easy I Assembly
Language Version
Easy I Memory
byte addressable
512
514
suma
count
Program
Data
100
102

## Slide 17: Programming the Easy I
Compute the sum of the even numbers between 1 and N
[Blackboard]

## Slide 18: Compute the sum of even numbers from 2 to N
Easy I Assembly Language & Machine Code Versions
Instruction Address | Assembly Code | Comment | Machine Code (binary)
100 | ANDi 0 |  | 0 00110 0000000000
102 | STOREi 512 | suma = 0 | 0 00100 1000000000
104 | ADDi 2 | count = 2 | 0 00111 0000000010
106 | STOREi 514 |  | 0 00100 1000000010
108 | LOOP: LOADi 514 | for(count=2;count<=N;count+=2){ | 0 00101 1000000010
110 | COMP |  | 0 00000 dddddddddd
112 | ADDi 1 | // add 2’s comp of count + N | 0 00111 0000000001
114 | ADD N | // N assumed in MEM[516] | 1 00111 1000000100
116 | BrNi END |  | 0 00010 0010000100
118 | LOADi 512 |  | 0 00101 1000000000
120 | ADD 514 | suma += count; | 1 00111 1000000010
122 | STOREi 512 |  | 0 00100 1000000010
124 | LOADi 514 |  | 0 00101 1000000010
126 | ADDi 2 |  | 0 00111 0000000010
128 | STOREi 514 |  | 0 00100 1000000010
130 | JUMPi LOOP | } | 0 00011 0001101100
132 | END: |  | 
dddddddddd = Don’t Care

## Slide 19: Easy I Data Paths
A
D
D
R
E
S
S
B
U
S
Typically, designing a processor is an iterative
(aka trial end error) process
A0
A bus
A
B
AC
PC
ALU
D
A
T
A
B
U
S
DI
16
16
16

## Slide 20: Processor Design Process
Done
Initial Data Path
Design c-unit
Measure
Happy?
Start
yes
no
Review
Data Path

## Slide 21: Easy I Memory Interface
CPU
MEMORY
address
data word
memory op
{R,W,NOP}
Memory
Bus

## Slide 22: Easy I Control Unit (Level 0 Flowcharts)
Fetch
Decode
FetchOp
Execute
Read next instruction
Determine what it does and
prepare to do it. Fetch operands.
Do it!
We will ignore indirect bit (assuming I = 0) for now

## Slide 23: Easy I Control Unit (Level 1 Flowcharts)
Fetch
Aopr
Sopr
Load
Store
Jump
BrN
Level 1: Each box may take several CPU cycles to execute
Reset
What?
Fetch Op

## Slide 24: What makes a CPU cycle?
CU Logic
FSM logic
state
Data Paths
Logic
ALU, latches, memory
Cycle time must accommodate signal propagation

## Slide 25: Easy I – Timing Example ALU Operation
A
B
AC
ALU
op
le
DI
le
CLK
DIle
DIout
ALUout
ACle
ACout

## Slide 26: Performance Assessment
IE ~ Instructions executed
CPI ~ Clock cycles per instruction
CT ~ Cycle time
Execution time = IE  CPI  CT
Key Performance
Metric

## Slide 27: Easy I Control Unit (Level 2 Flowcharts)
Each box may take only one CPU cycle to execute
0 → PC | 
reset1
PC → AO | 
PC + 2 → PC | 
reset2
RESET
fetch
Easy I Byte
Addressable
Can you tell why?
Invariant
At the beginning of the fetch cycle
AO holds address of instruction to be
fetched and PC points to following
instruction

## Slide 28: Easy I Control Unit (Level 3 Flowcharts)
AO → EAB | 
EDB → DI | 
branch on I and opcode | 
fetch
FETCH
Opcode must be an input to CU’s sequential circuit
Invariant
At the beginning of the fetch cycle
AO holds address of instruction to be
fetched and PC points to following
instruction
Memory Bus
Operation
fetchop
00 11x
opcode
aopr
sopr
load
store
brn
jump
00 00x
00 100
00 101
00 010
00 011
(I=0)
(I=1)

## Slide 29: Easy I Control Unit (Level 2 Flowcharts)
DI → ABUS → ALUA | 
AC → ALUB | 
ALU → AC | 
PC → AO | 
PC + 2 → PC | 
aopr
AOpr
fetch
Restore fetch
invariant

## Slide 30: Easy I Control Unit (Level 2 Flowcharts)
AC → ALUB | 
ALU → AC | 
PC → AO | 
PC + 2 → PC | 
sopr
SOpr
fetch

## Slide 31: Easy I Control Unit (Level 2 Flowcharts)
DI<0:9> → ABUS → AO | 
load1
DI → ABUS → ALUA | 
ALU → AC | 
PC → AO | 
PC + 2 → PC | 
load2
Load
fetch
AO → EAB | 
EDB → DI | 
load3
Must add path from DI to A0

## Slide 32: Easy I Control Unit (Level 2 Flowcharts)
DI<0:9> → ABUS → AO | 
store1
store2
Store
fetch
AC → EDB | 
AO → EAB | 
PC → AO | 
PC + 2 → PC | 

## Slide 33: Easy I Control Unit (Level 2 Flowcharts)
PC → AO | 
PC + 2 → PC | 
brn1
brn2
BrN
fetch
DI<0:9> → ABUS → PC | 
DI<0:9> → AO | 
PC + 2 → PC | 
AC:15
1 (AC<0)
0 (AC>0)
Bit 15 of AC input to the CU’s sequential circuit
Assume branch not
taken. Allow AC:15
to propagate.
Can we accomplish all this in 1 cycle? How?

## Slide 34: Inside the Easy-I PC
+2
Adder
ABUS
PC
0
pcsel
pcis
PC capable of loading and
incrementing
simultaneously
00
01
10
11
0
1
PC

## Slide 35: Easy I Control Unit (Level 2 Flowcharts)
DI<0:9> → PC | 
DI<0:9> → AO | 
PC + 2 → PC | 
jump
JUMP
fetch

## Slide 36: Easy I Data Paths (with control points)
le
A
D
D
R
E
S
S
B
U
S
A0
A bus
A
B
AC
PC
ALU
D
A
T
A
B
U
S
DI
le
op
is
sel
le
sel
sel
0
1
0
1
Is this necessary?

## Slide 37: Easy I - Control Unit
Control
Unit
Combinational
Logic
DataPaths
+ state
AC:15
OpCode
clock
I bit
Current State
EDBsel
PCis
DIle
AOle
AOsel
ACle
PCsel
MEMop
ALUop
Next State
17
11

## Slide 38: Easy I Control Unit State Transition Table (Part I)
Curr State | opcode | I | AC:15 |  | Next State | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
reset1 | xx xxx | x | x |  | reset2 | XXX | NOP | 01 | X | 0 | 0 | X | 0 | X
reset2 | xx xxx | x | x |  | fetch | XXX | NOP | 10 | 1 | 0 | 0 | 0 | 1 | X
fetch | 00 00x | 0 | x |  | sopr | XXX | NOP | 11 | X | 1 | 0 | X | 0 | X
fetch | 00 010 | 0 | x |  | brn1 | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
fetch | 00 011 | 0 | x |  | jump | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
fetch | 00 100 | 0 | x |  | store1 | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
fetch | 00 101 | 0 | x |  | load1 | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
fetch | 00 11x | 0 | x |  | aopr | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
aopr | 00 110 | x | x |  | fetch | AND | NOP | 10 | 1 | 0 | 1 | 0 | 1 | X
aopr | 00 111 | x | x |  | fetch | ADD | NOP | 10 | 1 | 0 | 1 | 0 | 1 | X
sopr | 00 000 | x | x |  | fetch | NOTB | NOP | 10 | 1 | 0 | 1 | 0 | 1 | X
sopr | 00 001 | x | x |  | fetch | SHRB | NOP | 10 | 1 | 0 | 1 | 0 | 1 | X

## Slide 39: Easy I Control Unit State Transition Table (Part II)
Current State | opcode | I | AC:15 |  | Next State | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
store1 | xx xxx | x | x |  | store2 | XXX | NOP | 11 | X | 0 | 0 | 1 | 1 | X
store2 | xx xxx | x | x |  | fetch | XXX | WR | 10 | 1 | 0 | 0 | 0 | 1 | 1
load1 | xx xxx | x | x |  | load2 | XXX | NOP | 11 | X | 0 | 0 | 1 | 1 | X
load2 | xx xxx | x | x |  | load3 | XXX | RD | 11 | X | 1 | 0 | X | 0 | X
load3 | xx xxx | x | x |  | fetch | A | NOP | 10 | 1 | 0 | 1 | 0 | 1 | X
brn1 | xx xxx | x | 0 |  | fetch | XXX | NOP | 10 | 1 | 0 | 0 | 0 | 1 | X
brn1 | xx xxx | x | 1 |  | brn2 | XXX | NOP | 10 | 1 | 0 | 0 | 0 | 1 | X
brn2 | xx xxx | x | x |  | fetch | XXX | NOP | 10 | 0 | 0 | 0 | 1 | 1 | X
jump | xx xxx | x | x |  | fetch | XXX | NOP | 10 | 0 | 0 | 0 | 1 | 1 | X
CU with 13 states => 4 bits of state

## Slide 40: Easy-I Control Unit – Some missing details
State | Encoding
reset1 | 0000
reset2 | 0001
fetch | 0010
aopr | 0011
sopr | 0100
store1 | 0101
store2 | 0110
load1 | 1000
load2 | 1001
load3 | 1010
brn1 | 1011
brn2 | 1100
jump | 1101
Operation | Code | Output
A | 000 | A
NOTB | 001 | not B
AND | 010 | A and B
ADD | 011 | A + B
SHRB | 100 | B / 2
4-bit Encodings for States
ALU Operation Table
We know how to implement this ALU !
Operation | Code
NOP | 00
ReaD | 01
WRite | 10
Control Bus Operation Table

## Slide 41: Easy I Control Unit State Transition Table (Part I)
Curr State | opcode | I | AC:15 |  | Next State | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
0000 | xx xxx | x | x |  | 0001 | XXX | 00 | 01 | X | 0 | 0 | X | 0 | X
0001 | xx xxx | x | x |  | 0010 | XXX | 00 | 10 | 1 | 0 | 0 | 0 | 1 | X
0010 | 00 00x | 0 | x |  | 0100 | XXX | 00 | 11 | X | 1 | 0 | X | 0 | X
0010 | 00 010 | 0 | x |  | 1011 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
0010 | 00 011 | 0 | x |  | 1101 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
0010 | 00 100 | 0 | x |  | 0101 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
0010 | 00 101 | 0 | x |  | 1000 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
0010 | 00 11x | 0 | x |  | 0011 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
0011 | 00 110 | x | x |  | 0010 | 010 | 00 | 10 | 1 | 0 | 1 | 0 | 1 | X
0011 | 00 111 | x | x |  | 0010 | 011 | 00 | 10 | 1 | 0 | 1 | 0 | 1 | X
0100 | 00 000 | x | x |  | 0010 | 001 | 00 | 10 | 1 | 0 | 1 | 0 | 1 | X
0100 | 00 001 | x | x |  | 0010 | 100 | 00 | 10 | 1 | 0 | 1 | 0 | 1 | X

## Slide 42: Easy I Control Unit State Transition Table (Part II)
Current State | opcode | I | AC:15 |  | Next State | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
0101 | xx xxx | x | x |  | 0110 | XXX | 00 | 11 | X | 0 | 0 | 1 | 1 | X
0110 | xx xxx | x | x |  | 0010 | XXX | 10 | 10 | 1 | 0 | 0 | 0 | 1 | 1
1000 | xx xxx | x | x |  | 1001 | XXX | 00 | 11 | X | 0 | 0 | 1 | 1 | X
1001 | xx xxx | x | x |  | 1010 | XXX | 01 | 11 | X | 1 | 0 | X | 0 | X
1010 | xx xxx | x | x |  | 0010 | 000 | 00 | 10 | 1 | 0 | 1 | 0 | 1 | X
1011 | xx xxx | x | 0 |  | 0010 | XXX | 00 | 10 | 1 | 0 | 0 | 0 | 1 | X
1011 | xx xxx | x | 1 |  | 1100 | XXX | 00 | 10 | 1 | 0 | 0 | 0 | 1 | X
1100 | xx xxx | x | x |  | 0010 | XXX | 00 | 10 | 0 | 0 | 0 | 1 | 1 | X
1101 | xx xxx | x | x |  | 0010 | XXX | 00 | 10 | 0 | 0 | 0 | 1 | 1 | X

## Slide 43: Easy I Control Unit (Level 3 Flowcharts)
fetchop1
FetchOp
00 11x
opcode
aopr
sopr
load
store
brn
jump
00 00x
00 100
00 101
00 010
00 011
Opcode must be an input to CU’s sequential circuit
Memory Bus
Operation
branch on opcode | 
fetchop2

## Slide 44: Building the Easy-I C-Unit 2 Approaches
Hardwired
  Apply well known sequential circuit techniques
Micro-programmed
  Treat state transition table as a program
  Build a new abstraction layer
The Microprogramming abstraction level
A program

## Slide 45: Building the Easy-I C-Unit Hardwired Approach
ROM
state
AC<15>
DI<10:14>
11
4
Data
Paths
Memory
Unit
control
bus
address
bus
data
bus
next
state
control
point
signals
5
Control
Unit
11
2
DI<15>

## Slide 46: Easy I Control Unit State Transition Table (Part II)
11-bit ROM address
17-bit ROM outputs
Current State | opcode | AC:15 |  | Next State | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
0101 | xx xxx | x |  | 0110 | XXX | 000 | 11 | X | 0 | 0 | 1 | 1 | X
0110 | xx xxx | x |  | 0111 | XXX | 010 | 10 | 1 | 0 | 0 | 0 | 1 | 1
1000 | xx xxx | x |  | 1001 | XXX | 000 | 11 | X | 0 | 0 | 1 | 1 | X
1001 | xx xxx | x |  | 1010 | XXX | 001 | 11 | X | 1 | 0 | X | 0 | X
1010 | xx xxx | x |  | 0010 | XXX | 000 | 10 | 1 | 0 | 1 | 0 | 1 | X
1011 | xx xxx | 0 |  | 0010 | XXX | 000 | 10 | 1 | 0 | 0 | 0 | 1 | X
1011 | xx xxx | 1 |  | 1100 | XXX | 000 | 10 | 1 | 0 | 0 | 0 | 1 | X
1100 | xx xxx | x |  | 0010 | XXX | 000 | 10 | 0 | 0 | 0 | 1 | 1 | X
1101 | xx xxx | x |  | 0010 | XXX | 000 | 10 | 0 | 0 | 0 | 1 | 1 | X
64 ROM
Addresses
with identical
content

## Slide 47: Programmable Logic Arrays

## Slide 49: Building the Easy-I C-Unit 2 Approaches
Hardwired
  Apply well known sequential circuit techniques
Micro-programmed
  Treat state transition table as a program
  Build a new abstraction layer
The Microprogramming abstraction level
A program

## Slide 50: Building the Easy-I C-Unit Micro-programmed Approach
00
11
01
10
reset1 | reset2 | 01 | xx | 00 | 01 | X | 0 | 0 | X | 0 | X
reset2 | fetch | 01 | xx | 00 | 10 | 1 | 0 | 0 | 0 | 1 | X
fetch | xxxx | 00 | xx | 00 | 11 | X | 1 | 0 | X | 0 | X
store1 | store2 | 01 | xx | 00 | 11 | X | 0 | 0 | 1 | 1 | X
store2 | fetch | 01 | xx | 10 | 10 | 1 | 0 | 0 | 0 | 1 | 1
load1 | load2 | 01 | xx | 00 | 11 | X | 0 | 0 | 1 | 1 | X
load2 | load3 | 01 | xx | 01 | 11 | X | 1 | 0 | X | 0 | X
load3 | fetch | 01 | xx | 01 | 11 | X | 1 | 0 | X | 0 | X
brn1 | xxxx | 11 | xx | 00 | 10 | 1 | 0 | 0 | 0 | 1 | X
brn2 | fetch | 01 | xx | 00 | 10 | 0 | 0 | 0 | 1 | 1 | X
jump | fetch | 01 | xx | 00 | 10 | 0 | 0 | 0 | 1 | 1 | X
Next State | Branch | ALU op | Mem OP | PC sel | PC is | DI le | AC le | AO sel | AO le | EDB sel
Opcode
Mapping
opcode
AC:15
Program
(Comb Logic)
DataPath Control
2
PC
0
1
fetch
4
brn2
unused

## Slide 51: Finding the first execute state Combinational Logic
Instruction | Opcode | AC:15 | First Execute State
Comp | 00 000 | x | sopr
ShR | 00 001 | x | sopr
BrN | 00 010 | 1 | brn1
Jump | 00 011 | x | jump
Store | 00 100 | x | store1
Load | 00 101 | x | load1
And | 00 110 | x | aopr
Add | 00 111 | x | aopr
Opcode
Mapping
opcode

## Slide 52: Summary
Instruction Set
Architecture
Processor
Implementation
What we know?
From
To
How do we get here
In the first place?
What Next?
Instruction Set
Design